## Slide 1: 本周工作内容汇报
2024年8月
黄子昱

## Slide 2
总block数不等于SM
/*
* Optimal grid size calculation is based on
* GH100: 8 GPCs, 72 TPCs (9 TPCs/GPC), 2 SMs/TPC, 144 SMs per full GPU
* Hence, maximum SMs per GPC = 18
*/
constexprint max_sm_per_gpc =18;
// Provided SM count could possibly be less than the assumed maximum SMs per GPC
auto cluster_size =cluster_shape.m() *cluster_shape.n();
intconst min_num_gpc = sm_count < max_sm_per_gpc ?1: sm_count / max_sm_per_gpc;
intconst max_cta_occupancy_per_gpc = max_sm_per_gpc - (max_sm_per_gpc % cluster_size);
cta_per_device = min_num_gpc * max_cta_occupancy_per_gpc;
// The calculation below allows for larger grid size launch for different GPUs.
intconst num_gpc_residual = sm_count < max_sm_per_gpc ?0: sm_count % max_sm_per_gpc;
intconst max_cta_occupancy_per_residual_gpc = num_gpc_residual - (num_gpc_residual % cluster_size);
cta_per_device += max_cta_occupancy_per_residual_gpc;
if (sm_count < cta_per_device) {
cta_per_device = sm_count;
}
if (raster_order ==RasterOrder::AlongN) {
launch_grid.y=possibly_truncate(
cta_per_device /cluster_shape.m(),
problem_blocks_total /cluster_shape.m());
更大的cluster，导致更少的可运行block（不使用DSM的情况下，cluster开更大只有坏处。）

## Slide 3
调整单GEMM计算顺序

## Slide 4
共享内存是怎么分配的？原先为什么使用227KB？原来是默认使用最大stage数！（可能可以调参优化）
setmaxreg，使得不同warp能够使用不同数量的寄存器。
性能结果
cutlass-origin是1.48ms，
my_version0是1.61ms，
my_version_persistent是1.59ms。
共享内存是怎么分配的？原先为什么使用227KB？原来是默认使用最大stage数！（可能可以调参优化）
setmaxreg，使得不同warp能够使用不同数量的寄存器。

## Slide 5
下周计划
进行两GEMM的融合
// 第一个GEMM，整体作为producer
if(producer){
producer
}
else{
consumer
}
cluster.sync(); // 中间结果存入共享内存
// 第二个GEMM，整体作为consumer
if(producer){
producer
}
else{
consumer
}